USING ZOIPER BIZ FOR WINDOWS FOR SENDING FAXES

The Zoiper Print to Fax Driver works on:

Windows 2000, Windows XP 32bit and Windows Vista32bit.

During the installation of Zoiper, the Printer Driver is being installed automatically.

When using Zoiper Biz on Windows 32bit, you  can send almost any document by using the Zoiper Printer driver.

Just open the document, open the printing dialogue and choose the "Zoipper Print to Fax" virtual device. This will open your Zoiper and send the file as a fax message.

When using Windows 64bit you have to convert the file to a TIFF file, then you will be able to send it as a FAX message by using Zoiper.

There are many tools for converting one type to another.

The guidelines for the TIFF files are:

200 dpi R6 (which is A4 and Letter combined, so either A4 or Letter is fine) portrait orientation, 1 bit per pixel.

We do support multi-page TIFF files and arbitrary resolutions and pixel depths.

Colour pages are automatically desaturated by luminance (standard YCrCb conversion), then dithered using Floyd-Steinberg to 1 bit per pixel.This has good effect and detail retaining for photos and pictures.

If a page is not in the 195-205 dpi resolution range it will be scaled automatically using Lanczos Sinc resampling to 200 dpi while retaining aspect. If the page size does not match R6 it will be cut where it is longer and white will be added where it is shorter. No scaling is used here.

Most of the TIFF image compressions are supported including JPEG-in-TIFF (but standalone JPEG files are not supported).

When not applicable like the case with Windows Vista 64bit, there are many tools available outside Zoiper, that can add that functionality.